## Slide 2
LECTURE 1

## Slide 3
Fundamentals of Electric Circuits: Ohm’s laws, Kirchhoff’s laws, Independent and Dependent sources, Analysis of simple circuits.
Network Theorems: Superposition theorem, Reciprocity theorem, Thevenin’s and Norton’s theorem, Maximum Power Transfer theorem.
Magnetic field, Concept of magnetic circuits, Magnetomotive force, Reluctance, Ampere’s circuital law and Biot-Savart law, Determination of B/H curve, Comparison of electric and magnetic circuit, Electromagnetic induction, Faraday’s laws of electromagnetic induction, Direction and Magnitude of induced E.M.F.
Self and mutual Inductance, Inductances in series and parallel, Energy stored in inductor, Capacitance, Capacitance in series and parallel, Relationship between charge, voltage and current, Energy stored in capacitor.
Transients with D.C. excitation.
Electrical Technology (EEC-01)
SYLLABUS

## Slide 4
Generation of alternating voltage and current, E.M.F. equation, Average and R.M.S. value, Phase and phase difference, Phasor representation of alternating quantity, Behaviour of A.C. circuits, Resonance in series and parallel R-L-C circuits.
Single-Phase Transformer, equivalent circuits, open circuit and short circuit tests.
Poly phase system, Advantages of 3-phase system, Generation of 3-phase voltages, Voltage, current and power in a star and delta connected systems, 3-phase balanced and unbalanced circuits, Power measurement in 3-phase circuits.
Electrical Technology (EEC-01)
SYLLABUS
Text Books:
1. Electrical & Electronic Technology by Hughes, Pearson Education India.
Reference Books:
1. Advanced Electrical Technology by H. Cotton, Reem Publication Pvt. Ltd
2. Electrical Engineering fundamentals by Vincent Deltoro, Pearson Education India.
1.

## Slide 5
Another Reference Books:
Electrical Engineering Concepts and Applications by S. A. Reza Zekavat;
Fundamentals of Electric Circuits by Charles K Alexander & Mathew N O Sadiku;
Electrical and Electronic Technology by Edward Hughes;
Electrical Circuits by Hyte and Kamarly;
Basic Electric Circuit Analysis by David E. Johnson, John L. Hilburn, Johnny R. Johnson and Peter D. Scott.
Engineering Circuit Analysis by J. David Irwin and Robert M. Nelms;
Linear Circuit Analysis by Raymond A. De Carlo and Pen-Min Lin.
Circuits and Networks by M.S. Sukhija and T. K. Nagsarkar;
Network Analysis by M.E. Van Valkenburg;
Networks and Systems by D. Roy Choudhury.
A text book of Electrical Technology by B. L. Thereja and A. K. Thereja;
Circuit Theory (Analysis and Synthesis) by A. Chakrabarty.
Electrical Technology (EEC-01)

## Slide 6
Fundamentals of Electric Circuits
Ohm’s Law
George Simon Ohm (1789 – 1854), a German physicist, investigated the relation between current and voltage in a resistor.
Difinition: Provided the physical conditions of a normal conductor remain the same, the potential difference necessary to send a current through the conductor is proportional to the current.
Potential difference, Current,
Fig. 1.1. Voltage-Current Relationship of a Resistor
In Fig. 1.1, the potential difference across the terminal of a resistor R is directly proportional to the current flowing through it.
;
is called the linear, time invariant, lumped resistance.
1

## Slide 7
Fundamentals of Electric Circuits
Ohm’s Law
Resistors
When a current flows in a material, the free electrons move through the material and collide with atoms.
The collision cause the electrons to lose some of their energy.
This loss of energy per unit charge is the drop in potential across the material.
The amount of energy lost by the electrons is related to the physical property of the material.
These collisions restrict the movement of electrons.
The property of a material to restrict the flow of electrons is called resistance.
The resistance is denoted by The symbol for the resistor is shown in Fig. 1.2.
Definition: A resistance is a two-terminal network component with terminal voltage directly proportional to current . The constant of proportionality is also called resistance.
2
Fig. 1.2. Symbol of resistor

## Slide 8
Fundamentals of Electric Circuits
Ohm’s Law
Resistors
The unit of resistance is ohm (Ω).
Ohm is defined as the resistance offered by the material when a current of one ampere flows between two terminals with one volt applied across it.
The volt ampere plot of a linear resistor is a straight line and that of many devices are nonlinear such as diode.
3
A resistor constructed of a semiconductor material such as silicon carbide have a characteristics of curve b in Fig. 3.
The device which exhibits nonlinear resistance is called a nonlinear resistor.
The resistor which is metallic conductor shows the voltage across the conductor is directly proportional to the current through it at constant temperature.
A resistor constructed of metal would obey ohm’s law and would have a characteristic that follow a straight line as given by a curve a of Fig. 1.3.
Fig. 1.3. Characteristics of resistor

## Slide 9
Fundamentals of Electric Circuits
Ohm’s Law
Resistors
Let a voltage as shown in Fig. 1.4. The reference polarity for and the reference direction for are shown in the figure.
4
Fig. 1.4. Sinusoidal Voltage applied to resistor
Ohm’s law is valid at any instant. Hence, the current is given by
The current is a sinusoidal alternating current and this is in phase with and having the same frequency.

## Slide 10
Fundamentals of Electric Circuits
Ohm’s Law
Resistors
5
The peak value of is
The power delivered by the source at any instant is
If is the time period of the impressed voltage, the average power per cycle is given by
watt

## Slide 11
Fundamentals of Electric Circuits
Ohm’s Law
Resistors
6
If is the instantaneous energy
Hence, the energy input from to is
joules
The energy input in n complete cycles is
joule, here is the frequency in hertz.
This energy is dissipated in the form of joule heat.

## Slide 12
Fundamentals of Electric Circuits
Ohm’s Law
When a sinusoidal current is applied to the resistor, the potential difference across it will be
The r.m.s value of voltage
where the r.m.s. value of current
Ohm’s law can also be expressed in terms of conductance (which is reciprocal of as
The r.m.s. value of current
Material whose conductivity depends not only on the value of the current flowing but also on its direction.
Silicon carbide possess a conductivity that varies over a wide range as the current through it is varied.
The well-known junction in a copper oxide rectifier has a conductivity which is high in one direction of current, low in the reverse direction and varies with current in either direction and varies with current in either case.
7

## Slide 13
Fundamentals of Electric Circuits
Kirchhoff’s Law
Electric circuit theory is based on two fundamental laws introduced by Kirchhoff.
These are Kirchhoff’s Voltage Law (abbreviated KVL) and Kirchhoff’s Current Law (abbreviated KCL)
Kirchhoff’s Voltage Law
It states that the algebraic sum of the voltage drops around any closed path of a circuit is zero at all instants of time.
In other words, around any closed path, at all instants of time, the sum of the voltage drops must equal the sum of the voltage rises.
A simple circuit is shown in Fig. 1.5 to illustrate the application of Kirchhoff’s Voltage Law.
8
Fig. 1.5. Circuit containing voltage source and circuit elements
The boxes contain the circuit elements. The reference polarities for voltages across the elements are shown.

## Slide 14
Fundamentals of Electric Circuits
Kirchhoff’s Law
Kirchhoff’s Voltage Law
The law follows from the principle of conservation of energy.
Let us start from the point A and move a unit positive charge in the direction of the arrow around the closed path.
The net change of energy for the movement of charge is zero.
The voltage drops around the closed path of the circuit is zero as voltage difference is equal to the ratio of energy change to unit charge.
A voltage drop is positive when we move from a ‘+’ polarity and is negative otherwise.
According to Kirchhoff’s law, the algebraic sum of the voltage drops must be zero.
This equation shows that the sum of the voltage drops is equal to the sum of the voltage rises.
9

## Slide 15
Fundamentals of Electric Circuits
Kirchhoff’s Law
Kirchhoff’s Current Law
It states that the algebraic sum of the currents entering a given point in a circuit is zero at all instants of time.
In other words, the sum of the currents entering a given point in a circuit equals the sum of the currents leaving that point at any instant of time.
This law is a consequence of the conservation of charge.
As charge can not accumulate at a point, the charge entering a point must leave it. The algebraic sum of the charge or its time derivative (which is the current) must thus be zero..
10
Fig. 1.6. Currents meeting at node
A simple circuit is shown in Fig. 1.6 to illustrate the application of Kirchhoff’s Current Law.
In Fig. 1.6, the currents and are entering the point and the currents and are leaving it.
Conventionally, the currents entering a point are taken to be positive.

## Slide 16
Fundamentals of Electric Circuits
Kirchhoff’s Law
Kirchhoff’s Current Law
11
According to Kirchhoff’s Current Law,
Kirchhoff’s Current Law is sometimes termed Kirchhoff’s Point Law.

## Slide 17
Fundamentals of Electric Circuits
Example – P1.1
Obtain the branch currents in the unbalanced bridge circuit of Fig. P1.1. Also determine the voltage drop across AC and the equivalent resistance between terminals A and C in the bridge circuit.
12
Fig. P1.1

## Slide 18
Solution of Example – P1.1
Fundamentals of Electric Circuits
The assumed direction of currents are shown in the figure.
Applying KVL in the loop ABDA, we get
or,
or,
Applying KVL in the loop BCDB, we get
or, 4
13
Fig. P1.1

## Slide 19
14
Applying KVL in the loop ABCEA, we get
Fundamentals of Electric Circuits
=4
or,
or,
Solving these equations and (we get
Solution of Example – P1.1

## Slide 20
Fundamentals of Electric Circuits
Then the branch currents are as follows:
Current in branch
Current in branch
Current in branch
Current in branch
Current in branch
Current in
Solution of Example – P1.1
15

## Slide 21
Fundamentals of Electric Circuits
The internal voltage drop of the cell being
Equivalent resistance between points and is the ratio of p.d. between points and to the current between these two points, The numerical value of the equivalent resistance becomes
Solution of Example – P1.1
[∵ The p.d. between points and =
16

## Slide 22
LECTURE 2

## Slide 23
Fundamentals of Electric Circuits
17
Analysis of simple circuits
The node method is based on kirchhoff’s current law (KCL).
The advantages of node method is that a minimum number of equations need to be solved to determine the unknown quantities.
Every junction in the network where two or more branches meet is regarded a node.
One of these is regarded as the reference node or datum node or zero potential node.
Hence, the number of simultaneous equations to be solved becomes (n-1) where n is the number of independent nodes.
These node equations often become simplified if all voltage sources are converted into current sources.

## Slide 24
Fundamentals of Electric Circuits
18
Analysis of simple circuits
The analysis of node method is illustrated through the circuit as shown in Fig. 1.7.
Fig. 1.7. Circuit used for node analysis.
There are four nodes, marked 0, 1, 2 and 3 in the network.
The node 0 is taken as the ground node or reference.
Let , and be the voltages at nodes 1, 2 and 3 respectively with respect to the reference.
Voltages , and are assumed to be positive.
The current entering node 1 is .
The current leaving this node is
Application of Kirchhoff’s current law gives
(1)

## Slide 25
Fundamentals of Electric Circuits
19
Analysis of simple circuits
Fig. 1.7. Circuit used for node analysis
Similarly, we get for node 2
(2)
and for node 3
(3)
Rearranging equations (1) through (3), we obtain
(4)
(5)
(6)
The self-admittance of a node is defined as the sum of the admittances connected to that node.
In the example, =, = and = .

## Slide 26
Fundamentals of Electric Circuits
20
Analysis of simple circuits
The coefficients of in Eq. (1), in Eq. (2) and (3) are the self-admittance of nodes 1, 2 and 3 respectively.
The coupling admittance between two nodes is the admittance connecting these two nodes.
In the example, the coefficient of in Eq. (4), is the coupling admittance between nodes 1 and 2. Similarly, between nodes 1 and 3 and so on.
It is observed that the self-admittance terms are positive while the sign of all the coupling admittance terms are negative.
The symbol for the coupling admittance between nodes h and k is
For linear bilateral elements, .
In the example, etc.
If there is no admittance coupling between nodes and, .

## Slide 27
Fundamentals of Electric Circuits
21
Analysis of simple circuits
The right-hand sides of the equation are positive when they denote current entering the nodes, and are negative when the current leave the nodes. These features follow from the reference directions and polarities chosen.
The right hand sides of some of the above equations may be zero.
Generalisation of these equations for a network having nodes of which one is a ground node yields
The self-admittances of nodes 1 through n are designated by , ,... respectively
The coupling-admittances are , ,… , ,…; .. , ,…
The incoming currents are , respectively.

## Slide 28
Fundamentals of Electric Circuits
22
Analysis of simple circuits
The voltages , …, can now be determined by solving the above equations by Cramer’s rule.
Cramer’s Rule
+
+
+
or,

## Slide 29
Fundamentals of Electric Circuits
23
Analysis of simple circuits
=
Similarly,
and

## Slide 30
Fundamentals of Electric Circuits
24
Analysis of simple circuits
Example – P1.2
Determine the output voltage, in the circuit as shown in Fig. P1.2 by using nodal method.
Fig. P1.2

## Slide 31
Fundamentals of Electric Circuits
25
Analysis of simple circuits
Solution of Example – P1.2
In the above circuit, 2 Ω and 5 Ω are in parallel and this is connected to 3 Ω in series. So, the equivalent resistance is 3+
Also 10 Ω and 2 Ω are in parallel and this is connected to 1 Ω in series. So, the equivalent resistance is 1+.
Fig. P1.2

## Slide 32
Fundamentals of Electric Circuits
26
Analysis of simple circuits
Solution of Example – P1.2
Assuming voltage at node and applying Kirchhoff’s current law in the circuit, we get
Volt

## Slide 33
Fundamentals of Electric Circuits
Analysis of simple circuits
Example – P1.3
In the network of Fig. P1.3, find the current through and voltage across 5 Ω resistor.
Fig. P1.3
27

## Slide 34
Fundamentals of Electric Circuits
Analysis of simple circuits
Solution of Example – P1.3
Apply KCL at node 1 and we get
or,
1
Apply KCL at node 2 and we get
or,
2
Apply KCL at node 3 and we get
or,
3
28

## Slide 35
Fundamentals of Electric Circuits
Analysis of simple circuits
Solution of Example – P1.3
In matrix form,
29

## Slide 36
Fundamentals of Electric Circuits
Analysis of simple circuits
Solution of Example – P1.3
The current through 5 Ω resistor is
The voltage drop across 5 Ω resistor is .
30

## Slide 37
Fundamentals of Electric Circuits
31
Analysis of simple circuits
Fig. 1.8. Circuit used for mesh analysis
Fig. 1.9. A tree of the circuit of Fig. 1.8
The analysis of mesh method is illustrated through the circuit as shown in Fig. 1.8.
The current supplied by the generator of voltage is to find out.
A suitable tree as shown in Fig. 1.9 is selected in such a way that the links of the tree contain the generator , the impedance , and the impedance .

## Slide 38
Fundamentals of Electric Circuits
32
Analysis of simple circuits
The network contains six branches and four nodes marked , , and .
The number of links or independent meshes is (.
These three links placed one at a time, form the meshes and respectively.
The link currents or the mesh currents in Fig. 1.8 are denoted by , and respectively.
Kirchhoff’s voltage law equation is to be written for each mesh. These equations are called mesh equations or loop equations.
These equations are to be solved to yield the link currents or the mesh currents.
The current in a tree branch which is common to two or more meshes is obtained by algebraically summing the associated mesh currents.

## Slide 39
Fundamentals of Electric Circuits
33
Analysis of simple circuits
Application of Kirchhoff’s Voltage Law to the three meshes gives the following three simultaneous equations.
(1)
(2)
(3)
Rearranging equations (1) through (3), we obtain
(4)
(5)
(6)
Fig. 1.8. Circuit used for mesh analysis

## Slide 40
Fundamentals of Electric Circuits
34
Analysis of simple circuits
Solving these equations, we get the desired current . The solution for and give the currents in impedances and respectively.
The current through is , that through is and that through is .
If any current turns out to be negative, it simply means that its actual reference direction is opposite to that chosen.
Since the current through any impedance is known, the voltages at the nodes are readily determined.
The sum of the impedances in going completely round a mesh is referred to as the self-impedance of the mesh.
The self-impedances of meshes 1 through are denoted by , , , …, respectively.
In the example, , and
The impedances that is common to two meshes is called the coupling impedance between the meshes.
The coupling impedance between meshes and is denoted by

## Slide 41
Fundamentals of Electric Circuits
35
Analysis of simple circuits
The coupling impedance between meshes and is denoted by .
Since, only linear bilateral elements are considered, hence .
In the example, , and
Generalisation of these equations for a network having meshes yields.
Here, the signs of the self-impedance terms are all positive.
The signs of some of the coupling impedance terms may be negative depending on the chosen reference directions of currents.

## Slide 42
Fundamentals of Electric Circuits
36
Analysis of simple circuits
The coupling impedance between meshes and is denoted by .
The sign before will be positive if the currents in the adjacent meshes and flow in the same direction through.
If they flow in the opposite direction through, the sign before is negative.
If there is no impedance common to meshes and , will be zero.
, ,….. are respectively the resultant voltages applied to meshes 1, 2,…n. If there is no resultant applied voltage in a particular, say , will be zero.
The currents , …, can now be determined by solving the above equations by Cramer’s rule.

## Slide 43
Fundamentals of Electric Circuits
Analysis of simple circuits
Example – P1.4
Find the current in the 3 Ω resistor of the circuit as shown in Fig. P1.4 by mesh method
Fig. P1.4
37

## Slide 44
The current through 3 Ω resistor is given by
Fundamentals of Electric Circuits
Analysis of simple circuits
Solution of Example – P1.4
Fig. P1.4.1
38

## Slide 45
LECTURE 3

## Slide 46
Fundamentals of Electric Circuits
39
The complicated networks can be simplified by successfully replacing delta meshes by equivalent star systems and vice versa.
The analysis of ‘delta/star and star/delta transformation’ is illustrated through the circuit as shown in Fig. 1.9.
(a)
(b)
Fig. 1.9. Circuit for delta/star and star/delta transformation

## Slide 47
Fundamentals of Electric Circuits
40
Three resistances, and are connected in delta fashion between terminals 1, 2 and 3 as shown in Fig. 12 (a).
These three resistances are replaced by the resistances, and , connected in star as shown in Fig. 12(b).
These two arrangements will be electrically equivalent if the resistance as measured between any pair of terminals is the same in both the arrangements.
First, consider the terminals of 1 and 2 in delta connection. There are two parallel paths. One having a resistance of and the other having a resistance.
Resistance between terminals 1 and 2 is
Now, consider star connection. The resistance between the same terminals 1 and 2 is

## Slide 48
Fundamentals of Electric Circuits
41
As terminal resistance have to be the same
(1)
Similarly, for terminals 2 and 3 and terminals 3 and 1, we get
(2)
and
(3)

## Slide 49
Fundamentals of Electric Circuits
42
Now, subtracting (2) from (1) and adding the result to (3), we get
(4)
Putting the value of in Eq. (1), we get
(5)
Putting the value of in Eq. (3), we get
(6)
So, resistance of each arm of the star is given by the product of the resistances of the two delta sides that meet at its end divided by the sum of the three delta resistances.

## Slide 50
Fundamentals of Electric Circuits
43
Dividing Eq. (4) by Eq. (5), we get
(7)
Similarly, dividing Eq. (5) by Eq. (6), we get
(8)
From Eqs. (7) and (8), we get

## Slide 51
Fundamentals of Electric Circuits
44
Putting values of and in Eq. (1), we get

## Slide 52
Fundamentals of Electric Circuits
45
or,
or,
Similarly,

## Slide 53
Fundamentals of Electric Circuits
46
Example – P1.5
Determine the equivalent resistance across X-Y of the circuit as shown in Fig. P1.5 by using star-delta transformation.

## Slide 54
Fundamentals of Electric Circuits
47
Solution of Example – P1.5
There are two star circuits in Fig. P1.5. One consisting of 5 Ω, 3 Ω and 4 Ω resistors and other one consisting of 6 Ω, 4 Ω and 8 Ω resistors.
Convert the star circuits into delta circuits so that the two delta circuits are in parallel.
The two star circuits and their equivalent circuits are shown below:
Ω
Ω
Ω
Fig. P1.5.1

## Slide 55
Fundamentals of Electric Circuits
48
Solution of Example – P1.5
The two star circuits and their equivalent circuits are shown below:
Ω
Ω
Ω
Fig. P1.5.2

## Slide 56
Fundamentals of Electric Circuits
49
Solution of Example – P1.5
The simplified circuit is shown in figure below
In the circuit, three resistors 10 Ω, 9.4 Ω and 17.3 Ω are in parallel.
Equivalent resistance = (10 ǁ 9.4 ǁ 17.3) = 3.78 Ω.
Resistors 13 Ω and 11.75 Ω are in parallel.
Equivalent resistance = (13 ǁ 11.75) = 6.17 Ω.
Resistors 26 Ω and 15.67 Ω are in parallel.
Equivalent resistance = (26 ǁ 15.67) = 9.78 Ω.
The simplified circuit is shown in Fig. below
The equivalent resistance

## Slide 57
LECTURE 4

## Slide 58
Fundamentals of Electric Circuits
50
Sources
Definition: The availability of electrical energy with network components called sources.
Example: Generators or alternators, that convert mechanical energy into electrical energy.
A battery that convert chemical energy into electrical energy.
Dependent Sources
Sources
Independent Sources
1. Independent Voltage Source
2. Independent Current Source
1. Voltage- Controlled Voltage Source (VCVS)
2. Voltage- Controlled Current Source (VCVS)
3. Current- Controlled Voltage Source (CCVS)
4. Current- Controlled Current Source (CCCS)

## Slide 59
Fundamentals of Electric Circuits
51
Sources
Independent Source: The sources which do not depend on any other quantity in the circuit are called independent sources.
Independent Voltage Source
A practical energy source such as battery in an automobile can maintain a voltage across its terminals which is relatively independent of the current required by the accessories under practical operating conditions.
The idealization of the device with a network component called an independent voltage source or more simply a voltage source.
The network symbol for the representation of an independent voltage source is shown in Fig. 1.10.
Fig. 1.10. Independent Voltage Source
The and marks inside the circle of the voltage source symbol identify the component as a voltage source.

## Slide 60
Fundamentals of Electric Circuits
52
Sources
Independent Source
Independent Voltage Source
Independent voltage source equation or source equation is
The component equation is graphically depicted in Fig. 1.11 for an independent voltage source with voltage to emphasize that the terminal voltage is independent of the terminal current.
It is observed from Fig. 1.11 that current has no effect on voltage
Fig. 1.11. Graphical representation of Independent Voltage Source

## Slide 61
Fundamentals of Electric Circuits
53
Sources
Independent Source
Independent Voltage Source
Definition: An independent voltage source is a two terminal network component with terminal voltage specified by a time function that is independent of the terminal current.
The definition of a voltage source represent that a short circuit can be considered to be a voltage source of value zero.
An independent voltage source can also be known as an ideal voltage source.

## Slide 62
Fundamentals of Electric Circuits
54
Sources
Independent Source
Independent Current Source
A few practical devices generate a current that is relatively independent of the terminal voltage over the normal range of operating voltage. The examples are as follows:
A constant current transformer used to supply power to incandescent street light.
An automobile alternator which provides relatively constant current under certain operating conditions.
We idealize such a device with a network component called an independent current source, or more simply a current source.
The network symbol used to represent an independent current source is shown in Fig. 1.12.
Fig. 1.12. Independent Current Source
The arrow inside the circle of the current source symbol identifies the component as a current source.

## Slide 63
Fundamentals of Electric Circuits
55
Sources
Independent Source
Independent Current Source
An Independent current source equation or source equation is
The component equation is graphically depicted in Fig. 1.13 for an independent current source with current to emphasize that the terminal current is independent of the terminal voltage.
It is observed from Fig. 1.13 that voltage has no effect on current
Fig. 1.13. Graphical representation of Independent Current Source

## Slide 64
Fundamentals of Electric Circuits
56
Sources
Independent Source
Independent Current Source
Definition: An independent current source is a two terminal network component with terminal current specified by a time function that is independent of the terminal voltage .
The definition of a current source represent that an open circuit can be considered to be a current source of value zero
An independent current source can also be known as an ideal current source.

## Slide 65
Fundamentals of Electric Circuits
57
Sources
Dependent Source
Many electrical systems take a small amount of electric power from one source and use this to control the delivery of a large amount of electric power from another source.
The example of dependent source is an amplifier used in a tape player. The working principle of the amplifier is given below:
The magnetized tape moving past the tape ahead, which consists of magnetic material and a small coil of wire, generates a very small voltage signal that delivers a small fraction of a watt to the amplifier.
This low power signal ultimately controls the delivery of tens of watts to the speaker system.
The power to the speaker is obtained from the amplifier power source: a car battery or an electrical outlet.
The ability to control the delivery of power is modelled by the introduction of four terminal network components called dependent sources or controlled sources.

## Slide 66
Fundamentals of Electric Circuits
58
Sources
Dependent Source
Voltage- Controlled Voltage Source (VCVS)
A tape player amplifier is an example of voltage-controlled voltage source. The amplifier generate a large voltage across two terminals that is intended to be proportional to a smaller voltage established across other two terminals.
A practical voltage amplifier is idealized with a four terminal network component called a voltage controlled voltage source (VCVS).
The network symbol as shown in Fig. 1.14 is used to represent a VCVS.
Fig. 1.14. Voltage- Controlled Voltage Source
The and marks inside the diamond of the component symbol identify the component as a voltage source.

## Slide 67
Fundamentals of Electric Circuits
59
Sources
Dependent Source
Voltage- Controlled Voltage Source (VCVS)
An equivalent definition is given by the following component equation or control equation.
Control Equation:
It is observed that voltage depends only on the constant , a dimensionless constant called the voltage gain and the control voltage .
Current can affect voltage only if it affects voltage.
Definition: A voltage controlled voltage source is a four-terminal network component that establishes a voltage between two points and in the circuit that is proportional to a voltage between two points and .

## Slide 68
Fundamentals of Electric Circuits
60
Sources
Dependent Source
Voltage- Controlled Voltage Source (VCVS)
Example of VCVS
Determine voltage in the circuit as shown in Fig. 1.15
Fig. 1.15. Test figure of Voltage- Controlled Voltage Source
Solution for Example of VCVS
Kirchhoff’s voltage law easily established that

## Slide 69
Fundamentals of Electric Circuits
61
Sources
Dependent Source
Voltage- Controlled Current Source (VCCS)
The field-effect transistor is an example of voltage-controlled current source. This electronic device permit the control of a current directly with a voltage.
The device is idealized with a four terminal network component called a voltage-controlled current source (VCCS).
The network symbol as shown in Fig. 1.16 is used to represent a VCCS.
Fig. 1.16. Voltage- Controlled Current Source
The arrow inside the diamond of the component symbol identifies the component as a current source.

## Slide 70
Fundamentals of Electric Circuits
62
Sources
Dependent Source
Voltage- Controlled Current Source (VCCS)
An equivalent definition is given by the following component equation or control equation.
Control Equation:
It is observed that current depends only on the control voltage and the constant , called the transconductance or mutual conductance.
Constant has dimension of ampere per volt or Siemens (S).
Definition: A voltage-controlled current source is a four-terminal network component that establishes a current in a branch of the circuit that is proportional to the voltage between two points and .

## Slide 71
Fundamentals of Electric Circuits
63
Sources
Dependent Source
Voltage- Controlled Current Source (VCCS)
Example of VCCS
Determine the current in the circuit as shown in Fig. 1.17
Fig. 1.17. Test figure of Voltage- Controlled Current Source
Solution for Example of VCCS

## Slide 72
Fundamentals of Electric Circuits
64
Sources
Dependent Source
Current- Controlled Voltage Source (CCVS)
The resistor is an example of current-controlled voltage source. This device permits the control of voltage across one branch with current through another branch in the circuit.
The device is idealized with a four terminal network component called a current-controlled voltage source (CCVS).
The network symbol as shown in Fig. 1.18 is used to represent a CCVS.
Fig. 1.18. Current- Controlled Voltage Source
The and marks inside the diamond of the component symbol identify the component as a voltage source.

## Slide 73
Fundamentals of Electric Circuits
65
Sources
Dependent Source
Current-Controlled Voltage Source (VCCS)
An equivalent definition is given by the following component equation or control equation.
Control Equation:
It is observed that voltage depends only on the control current and the constant, called the transresistance or mutual resistance.
Constant has the dimension of volt per ampere or ohm (Ω).
Definition: A current-controlled voltage source is a four-terminal network component that establishes a voltage between two points and in the circuit that is proportional to current in some branch of the circuit.

## Slide 74
Fundamentals of Electric Circuits
66
Sources
Dependent Source
Current- Controlled Voltage Source (CCVS)
Example of CCVS
Determine voltage in the circuit as shown in Fig. 1.19.
Fig. 1.19. Test figure of Current-Controlled Voltage Source
Solution for Example of CCVS

## Slide 75
Fundamentals of Electric Circuits
67
Sources
Dependent Source
Current- Controlled Current Source (CCCS)
The bipolar junction transistor is an example of current-controlled current source. This device permits the control of one current with another
The device is idealized with a four terminal network component called a current-controlled current source (CCCS).
The network symbol as shown in Fig. 1.20 is used to represent a CCCS.
Fig. 1.20. Current- Controlled Current Source
The arrow inside the diamond of the component equation identifies the component as a current source.

## Slide 76
Fundamentals of Electric Circuits
68
Sources
Dependent Source
Current-Controlled Current Source (CCCS)
An equivalent definition is given by the following component equation or control equation.
Control Equation:
It is observed that current depends only on the control current and the dimensionless , called the current gain.
Definition: A current-controlled current source is a four-terminal network component that establishes a current in one branch of a circuit that is proportional to current in some branch of the network.

## Slide 77
Fundamentals of Electric Circuits
69
Sources
Dependent Source
Current- Controlled Current Source (CCCS)
Example of CCCS
Determine current in the circuit as shown in Fig. 1.21.
Fig. 1.21. Test figure of Current-Controlled Current Source
Solution for Example of CCCS

## Slide 78
Fundamentals of Electric Circuits
70
Equivalence of voltage and current sources
Fig. 1.22. Equivalence of Voltage and Current Sources
The equivalence of voltage and current sources is shown in Fig. 1.22.
In Fig. 1.22(a), a voltage source, in series with an impedance, supplies a current to a load impedance
represent the internal impedance of the source.
(a)
(b)

## Slide 79
Fundamentals of Electric Circuits
71
Equivalence of voltage and current sources
where .
The circuit in Fig. 1.22(b) represents Eq. (2). Here, is the current delivered by the voltage source when the terminals ab are short-circuited.
The circuits shown in Fig. 1.22(a) & (b) are equivalent so far as the current through the load impedance is concerned.
The mutual conversion of voltage & current sources is positive when is finite other than zero.
The phasor equation for the load voltage is
(1)
(2)

## Slide 80
Fundamentals of Electric Circuits
72
Equivalence of voltage and current sources
Example – P1.6
Determine, , , and for the network as shown in Fig. P1.6, if no other components are connected to terminals and .
Fig. P1.6

## Slide 81
Fundamentals of Electric Circuits
73
Equivalence of voltage and current sources
Solution of Example – P1.6
=
Independent and Dependent Sources are active components.
The source which cannot supply positive average power, these are passive components.
A network that contains one or more active components is an active network.
A passive network contains only passive components.
Some physical devices convert electrical energy into heat or store energy in electric or magnetic fields. We model the properties of the devices with network components called elements.

## Slide 82
Fundamentals of Electric Circuits
74
Equivalence of voltage and current sources
Example – P1.7
Fig. P1.7
Find in the circuit of Fig. P1.7. Check the power balance condition.

## Slide 83
Fundamentals of Electric Circuits
75
Equivalence of voltage and current sources
Solution of Example – P1.7
Applying KVL in the given loop
The dependent source offers a terminal voltage of =
In the circuit, power is supplied by 6 V and 10 V source while power is absorbed by 110 resistor (dissipating heat) and the dependent source.

## Slide 84
Fundamentals of Electric Circuits
76
Equivalence of voltage and current sources
Solution of Example – P1.7
Thus power supplied by 6 V source
Power supplied by 10 V source
Total power supplied
Power absorbed by the dependent source is and
power absorbed by the 110 Ω resistance is 110
Total power absorbed
Thus, the total power balance is maintained.

## Slide 85
Fundamentals of Electric Circuits
77
Analysis of simple circuits
Example – P1.8
Find the loop currents and of the circuit in Fig. P1.8 by mesh method.
Fig. P1.8

## Slide 86
Fundamentals of Electric Circuits
78
Analysis of simple circuits
Fig. P1.8
Solution of Example – P1.8
In loop 1, mesh analysis gives
or,
(1)
In loop 2, mesh analysis gives
or,
(2)
In loop 3, mesh analysis gives
(3)
Answer
From loop 3, we also get
(4)